## Slide 1: Final project report
111061634 曾淳浩

## Slide 2: Outline
1.Introduce convolution code and Viterbi decoding
2.System Architecture
3.HLS report
4.RISCV – vp report
5.Discussion problem

## Slide 3: Viterbi decoder
Viterbi decoder is used to decode convolution code or trellis code.
The Viterbi algorithm is the most resource-consuming, but it does the maximum likelihood decoding.

## Slide 4
System Architecture

## Slide 5
Encoder
(2, 1, 3) convolutional code
D u output(x1 x2)
0 0 0 1 11
1 1 1 0 00

## Slide 6: Channel
Double to binary

## Slide 7
State diagram(decoder)
State diagram stores in Viterbi decoder let every nodes know output value and input node .

## Slide 8
Algorithm
1.Caculate hamming distance between received bits (after channel) and two input-nodes output.
2. Add hamming distance to input node’s accumulate path and choice small one.
3.Update accumulate path and decoded bits
Repeat 8 times each cycle

## Slide 9
Memory in decoder

## Slide 10
HLS report

## Slide 11
Behavior simulation
SNR (db) | Channel error | Decoded error | BER
1 | 12133 | 8400 | 0.1680
2 | 9767 | 5177 | 0.1342
3 | 7524 | 2537 | 0.0762
4 | 5513 | 1101 | 0.0348
5 | 3716 | 363 | 0.0125
6 | 2257 | 90 | 0.0018
N = 50000bits

## Slide 12
RTL simulation version1
Clock cycle 10ns
N=50000 SNR= 3(dB)
 | Total run time | Area
BASIC | 1338596430ns | 40126.6
PIPE_LINE_UNROLL II=2 | 1501010ns | 12178.9
PIPE_LINE_UNROLL II=3 | 2001320 ns | 11458.9

## Slide 13
RTL simulation version2
 | Total run time | Area
BASIC | 1338596430ns | 37026.6
PIPE_LINE_UNROLL II=2 | 1501010ns | 8825.0
PIPE_LINE_UNROLL II=3 | 2001320 ns | 8353.7
1.Loop variable sizing
1.buffer sizing

## Slide 14
RTL simulation version3
 | Total run time | Area
BASIC | 938546430ns | 41026.6
PIPE_LINE_UNROLL II=2 | 1501010ns | 8825.0
PIPE_LINE_UNROLL II=3 | 1501010ns | 7421.8
1.Use latency constrain to while loop
同時做pipe line (II=3)和latency constrain 會將時間壓縮到與(II=2)相同 但得到更小area